## Slide 1
AN INTRODUCTION TO CODING THEORY WITH LINEAR ALGEBRA
Team 17:
•Agrim Mittal (2022101040)
•Bipasha Garg (2022111006)
•Palle Sreeja (2022101081)

## Slide 2
INTRODUCTION
In coding theory, linear codes are a type of error-correcting codes defined as subsets of a vector space over a finite field. The vectors in the code are n-dimensional and represent the code-words, while k represents the dimension or the number of information symbols in each code-word. The vectors in a linear code can be represented as binary strings or sequences of symbols from the finite field F.
Linear Algebra plays a fundamental role in coding theory, particularly in the design and analysis of error-correcting codes. The project explores concepts like linear codes, parity check matrices, and syndromes, and investigates how linear algebraic tools can be used to encode and decode messages in the presence of noise or transmission errors. The project emphasizes the application of linear algebra in ensuring reliable and secure communication.

## Slide 3
The code is characterized by the following properties:
•Closure under vector addition
•Closure under scalar multiplication
The code-words are obtained by applying a linear transformation or encoding function to the information symbols, often represented by a generator matrix. Linearity is a crucial property of linear codes.
Linear codes are particularly useful for error detection and correction. By designing the generator matrix or parity check matrix of a linear code, it is possible to detect and correct a certain number of errors or erasures that may occur during message transmission

## Slide 4
TOPICS COVERED
  GENERATOR MATRICES
  COSET ARRAY DECODING
  PARITY-CHECK MATRIX
  SYNDROME DECODING
  PERFECT CODES
  HAMMING CODES
  REED SOLOMON CODES
  NETWORK COMMUNICATION

## Slide 5
GENERATOR MATRIX
Linear codes can be entirely defined by listing only the basis vectors of the code’s subspace, as opposed to listing every single code-word. This generator matrix can be obtained from the matrix of the entire code by the use of row reduction. A binary [n, 2^K ]−code will reduce to a generator matrix of dimensions k × n. The code can then be re-generated by creating all linear combinations of the rows of the generator matrix.

## Slide 6
COSET ARRAY DECODING
The algorithm works by constructing cosets of the code and finding the coset with the minimum weight, which corresponds to the most likely transmitted code-word.
  The method involves:
  Listing elements of coset
  Finding coset leader
  Decoding

## Slide 7
PARITY CHECK MATRICES
Parity-check matrices are used to determine whether an encoded message contains any errors by performing mathematical operations on the received code-word.
The parity-check matrix, denoted as H, is an important matrix used in linear coding theory. It is constructed such that any code-word in the linear code is orthogonal to the rows of the parity-check matrix. In other words, the dot product of any code-word and any row of the parity-check matrix is zero. This property allows the parity-check matrix to detect errors in the received code-word.
It’s important to note that parity-check matrices are typically designed to detect errors, but not correct them. For error correction, other techniques such as syndrome decoding or maximum likelihood decoding algorithms are employed in combination with the parity-check matrix.

## Slide 8
SYNDROME DECODING
Syndrome decoding is a highly efficient method of decoding a linear code over a noisy channel, i.e., one on which errors are made. In essence, syndrome decoding is minimum distance decoding using a reduced lookup table. This is allowed by the linearity of the code. The parity-check matrix is especially useful for generating the syndrome of a given coset.
Syndrome decoding is useful for correcting multiple errors.

## Slide 9
PERFECT CODE
A perfect code is a code in which every possible word of a specified length is a valid code-word, and the minimum distance between any two code-words is maximized. This property ensures that no valid message is misinterpreted as an error, and the codes can correct errors up to a certain threshold.
Perfect codes find extensive applications in the transmission of digital data. Due to their ability to achieve maximum error correction, they provide a high level of reliability in critical communication systems. Perfect codes are used in various domains, including satellite communication, data storage systems, and telecommunications. Their efficiency in terms of error correction and reliable data transmission make them indispensable in applications where accuracy and integrity are paramount.

## Slide 10
HAMMING CODES
The general idea for achieving error detection and correction is to add some extra data with the message, which receivers can use to check consistency of the delivered message, and to recover data determined to be corrupted . Hamming code can only correct single bit errors.
The process involves:
  Checking the parity bits
  Finding the incorrect bit
  Error correction

## Slide 11
Reed-Solomon Codes
Reed-Solomon Codes are used to correct multiple errors from the code. They are used to protect data from defects in the storage or transmission media. The Reed-Solomon code is crucial to the success of the audio CD, allowing CD players to interpolate data lost due to scratches or dust on the disks

## Slide 12
NETWORK COMMIUNICATION
The process of network communication using coding theory involves encoding the data at the source, transmitting the code-word over the channel, and decoding the code-word at the destination to recover the original data. The use of error-correcting codes helps ensure that the transmitted data is reliable and accurate, even in the presence of errors introduced by the channel.
Methodology:
  Code Selection
  Encoding
  Modulation and Channel Coding
  Transmission
  Reception
  Decoding
  Error detection and Correction
  Extraction

## Slide 13
THANK YOU
TEAM 17
AGRIM MITTAL [2022101040]
Study of Generator Matrices and its implementation using example
Correction of multiple errors using syndrome decoding
Study of Reed Solomon Codes and its application
PALLE SREEJA [2022101081]
Introduction of coding theory
Study of Parity-Check Matrix and its procedure to encode data
Study of Perfect codes
BIPASHA GARG [2022111006]
Study of Coset array decoding and the method to use it
Study of Hamming code and it’s working
Implementation of coding theory in making network communication reliable and secure